## Slide 1: Track Structural Analysis Rigid Frame
June 2021

## Slide 2: F.E model
Total mass (include box) = 2 [Ton] (Half model)
Half model - Symmetry

## Slide 3: F.E model – Mass Distribution
Mass = 1.275[Ton] (Half model)

## Slide 4: F.E model – Connections
Vertical connection (Only Y direction)
Longitudinal connection (Only X direction)

## Slide 5: Material distribution
Red parts – Creusabro 4800
Yellow parts – ST52
Blue parts – Rigid
Green parts – casting Steel
Turquoise parts – ST37
M45 Bolts – 4340

## Slide 6: Thickness distribution [mm]

## Slide 7: mechanical properties
Steel 4340 | Steel Casting | Steel ST37 | Steel ST52 | Steel Creusabro 4800 | 
0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 
7800 | 7800 | 7800 | 7800 | 7800 | 
21000 | 21000 | 21000 | 21000 | 21000 | 
80 | 21 | 25 | 35 | 90 | 
94 | 42 | 37 | 52 | 120 | 
18 | 20 | 25 | 15 | 12 | 
Steel 4340 | Steel Casting | Steel ST37 | Steel ST52 | Steel Creusabro 4800 | 
0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 
7800 | 7800 | 7800 | 7800 | 7800 | 
21000 | 21000 | 21000 | 21000 | 21000 | 
80 | 21 | 25 | 35 | 90 | 
94 | 42 | 37 | 52 | 120 | 
18 | 20 | 25 | 15 | 12 | 

## Slide 8
Load Cases
Nonlinear analysis
  Longitude (X axis) : -60g acting on all parts
60g

## Slide 9: Boundary conditions
Wheels area fix in vertical Y direction
Front area fix in longitude X direction
Symmetry B.C (Half Model)

## Slide 10: Nonlinear Static acceleration

## Slide 11
60g Longitude -X
Displacement magnitude [mm]

## Slide 12
Creusabro 4800 Parts
60g Longitude -X
Von Misses Stress [kg/mm2]
Singular point
The actual Max stress is 70.0

## Slide 13
Creusabro 4800 Parts
60g Longitude -X
Von Misses Stress [kg/mm2]

## Slide 14
Creusabro 4800 Parts
60g Longitude -X
Von Misses Stress [kg/mm2]

## Slide 15
Creusabro 4800 Parts
60g Longitude -X
Von Misses Stress [kg/mm2]

## Slide 16
Creusabro 4800 Parts
60g Longitude -X
Von Misses Stress [kg/mm2]

## Slide 17
Creusabro 4800 Parts
60g Longitude -X
Von Misses Stress [kg/mm2]

## Slide 18
Creusabro 4800 Parts
60g Longitude -X
Von Misses Stress [kg/mm2]

## Slide 19
Creusabro 4800 Parts
60g Longitude -X
Von Misses Stress [kg/mm2]
Singular point
The actual Max stress is 66.5

## Slide 20
ST52 Parts
60g Longitude -X
Von Misses Stress [kg/mm2]

## Slide 21
ST52 Parts
60g Longitude -X
Von Misses Stress [kg/mm2]

## Slide 22
ST52 Parts
60g Longitude -X
Von Misses Stress [kg/mm2]

## Slide 23
ST52 Parts
60g Longitude -X
Von Misses Stress [kg/mm2]

## Slide 24
ST37 Parts
60g Longitude -X
Von Misses Stress [kg/mm2]

## Slide 25
ST37 Parts
60g Longitude -X
Von Misses Stress [kg/mm2]

## Slide 26
60g Longitude -X
Bolt Forces [Kg]

## Slide 27
60g Longitude -X
Bolt Moments [Kg*mm]

## Slide 28
60g Longitude -X
TL Forces [Kg]

## Slide 29
60g Longitude -X
TL Moments [Kg*mm]

## Slide 30
60g Longitude -X
Bolt axial Forces [Kg]

## Slide 31
60g Longitude -X
Bolt friction Forces [Kg]

## Slide 32
60g Longitude -X
Bolt Moments [Kg*mm]

## Slide 33
60g Longitude -X
Bolt Forces [Kg]

## Slide 34
60g Longitude -X
Bolt axial force [kg]

## Slide 35
60g Longitude -X
Force Welding [Kg]
9483

## Slide 36
60g Longitude -X
Force Welding [Kg]

## Slide 37
60g Longitude -X
Force Welding [Kg]

## Slide 38
60g Longitude -X
Force Welding [Kg]

## Slide 39
60g Longitude -X
Moment Welding [Kg*mm]

## Slide 40
60g Longitude -X
Force Welding [Kg]

## Slide 41
60g Longitude -X
Moment Welding [Kg*mm]

## Slide 42
60g Longitude -X
Force Welding [Kg]

## Slide 43
60g Longitude -X
Moment Welding [Kg*mm]

## Slide 44
Stress Summary
Safety Factor | Allowable Stress | Max Stress | Material | Load case
1.71 | 120 UTS | 70.0 | Creusabro 4800 | 60g Longitude -X
1.49 | 52 UTS | 34.9 | ST52 | 60g Longitude -X
1.48 | 37 UTS | 25 | ST37 | 60g Longitude -X
Safety Factor |  |  | Material | Load case
1.71 | 120 UTS | 70.0 | Creusabro 4800 | 60g Longitude -X
1.49 | 52 UTS | 34.9 | ST52 | 60g Longitude -X
1.48 | 37 UTS | 25 | ST37 | 60g Longitude -X

## Slide 45
Bolts Calculation
    6 Bolts M14 - Class 10.9
    Tightening force 7951 Kg
    Effective area – As=115 mm²
    Tensile Strength 104 [kg/mm2]
Max. tension force – 2546 Kg
    Total tension force – 7951+2546/4 = 8588 Kg
σ = F/As = 8588/115 = 74.7 kg/mm2
S.F = 104/74.7 = 1.4

## Slide 46
Bolts Calculation
    Tensile calculation:
    2 Bolts M45 – Steel 4340
    Effective area – As=1256 mm²
    Tensile Strength 94 [kg/mm2]
Max. compression force – 43444 Kg
σ = F/As = 43444/1256 = 34.6 kg/mm2
S.F = 94/34.6 = 2.7
    Thread calculation:
    Number of threads - 3
    Thread pitch 4mm
    Shear area – A=1507 mm²
    Tensile Strength 94 [kg/mm2]
    Shear Strength 94*0.6 = 56.4 [kg/mm2]
Max. compression force – 43444 Kg
σshear = F/A = 43444/1507 = 28.8 kg/mm2
S.F = 56.4/28.8 = 1.96

## Slide 47
Bolt Buckling Calculation
Max. compression force – 43444 Kg
E = 21000 Kg/mm2
54.6mm
    Buckling calculation
I = 402578 mm4
L = 54.6 mm
K = 2
S.F for Buckling = 6,997,192/43444 = 161

## Slide 48
Bolts Calculation
    4 Bolts M36 - Class 10.9
    Effective area – As=506 mm²
    Tensile Strength 104 [kg/mm2]
Max. tension force – 36906 Kg
σ = F/As = 36906/506 = 72.9 kg/mm2
S.F = 104/72.9 = 1.43
    Thread calculation:
    Number of threads - 3
    Thread pitch 4mm
    Shear area – A=948 mm²
    Tensile Strength 104 [kg/mm2]
    Shear Strength 104*0.6 = 62.4 [kg/mm2]
Max. tension force – 36906 Kg
σshear = F/A = 36906/948 = 38.9 kg/mm2
S.F = 62.4/38.9 = 1.6
    Tensile calculation:

## Slide 49
Pins Calculation
    2 Pins M45 – Steel 4340
    Effective area – As=1590 mm²
    Tensile Strength 104 [kg/mm2]
    Shear Strength 94*0.6 = 56.4 [kg/mm2]
Max. shear force – 45657 Kg
σshear = F/As = 45657/1590 = 28.7 kg/mm2
S.F = 56.4/28.7 = 1.96

## Slide 50
Bolts Calculation
    42 Bolts M16 - Class 12.9 - Work only in tension (Shear is taken by friction and 2 pins)
    Tightening force 12946 Kg
    Effective area – As=157 mm²
    Tensile Strength 122 [kg/mm2]
Max. tension force – 6769 Kg
    Total tension force – 12946+6769/4 = 14,638 Kg
σ = F/As = 14638/157 = 93 kg/mm2
S.F = 122/93 = 1.3

## Slide 51
Bolts Calculation
    8 Bolts M16 - Class 12.9 Work only in tension
    (Shear is taken by friction)
    Tightening force 12946 Kg
    Effective area – As=157 mm²
    Tensile Strength 122 [kg/mm2]
Max. tension force – 6618 Kg
    Total tension force – 12946+6618/4 = 14600 Kg
σ = F/As = 14600/157 = 93 kg/mm2
S.F = 122/93 = 1.3

## Slide 52
Welding Calculation
    Welding Hight = 8mm
    Welding Area = ((140X8))X4 = 4480 mm²
Max. tension force – 9483 Kg
Yield Strength welds 45 [kg/mm2]
σ = F/As = 9483/4480 = 2.1 kg/mm2
S.F = 45/2.1 = 21.4
140mm
140mm

## Slide 53
Welding Calculation
    Welding Hight = 10mm
    Welding Area = ((105X10))X2 = 2100 mm²
Max. tension force – 30406 Kg
Yield Strength welds 45 [kg/mm2]
σ = F/As = 30406/2100 = 14.5 kg/mm2
S.F = 45/14.5 = 3.1
105mm

## Slide 54
Welding Calculation
    Welding Hight = 15mm
    Welding Area = ((50X15))X2 = 1500 mm²
Max. tension force – 23273 Kg
Yield Strength welds 45 [kg/mm2]
σ = F/As = 23273/1500 = 15.5 kg/mm2
S.F = 45/15.5 = 2.9
50mm

## Slide 55
Welding Calculation
    Welding Hight = 20mm
    Welding Area = (80X20X2)X2 = 6400 mm²
Max. tension force – 46818 Kgf
Yield Strength welds 45 [kg/mm2]
σF = F/As = 46818/6400 = 7.3 kg/mm2
S.F = 45/7.3 = 6.2
80mm
80mm

## Slide 56
Welding Calculation
    H (Welding Hight) = 20X2 = 40 [mm]
Moment X = 16905636 [kg*mm]
Yield Strength welds 45 [kg/mm2]
σMx = (6*Mx)/(H*L2) = (6*16905636)/(40*4082) = 15.2 kg/mm2
S.F = 45/15.2 = 3
L = 408mm

## Slide 57
Welding Calculation
90mm
D = 83mm
    H (Welding Hight) = 10X2 = 20mm
    Welding Area = (90X20)X2 = 3600 mm²
Max. force = √(51192 + 47492) = 6983 [Kg]
Moment X = 315880 [kg*mm]
Moment Y = 178444 [kg*mm]
Yield Strength welds 45 [kg/mm2]
σF = FT /As = 6983/3600 = 1.9 kg/mm2
S.F = 45/6.3 = 7.1
σcombined = √(σF 2 + σMy 2 + σMx 2) = 6.3 kg/mm2
σMy = (My)/(L*D*H) = (178444)/(90*83*20) = 1.2 kg/mm2
σMx = (3*Mx)/(H*L2) = (3*315880)/(20*902) = 5.9 kg/mm2

## Slide 58
Welding Calculation
    H (Welding Hight) = 10mm
    Welding Area = (140X10)X2 = 2800 mm²
Max. force = √(95442 + 48142) = 10689 [Kg]
Moment X = 726800 [kg*mm]
Moment Y = 218813 [kg*mm]
Yield Strength welds 45 [kg/mm2]
σF = FT /As = 10689/2800 = 3.8 kg/mm2
S.F = 45/12 = 3.75
L = 140mm
σcombined = √(σF 2 + σMy 2 + σMx 2) = 12 kg/mm2
σMy = (My)/(L*D*H) = (218813)/(140*83*10) = 1.9 kg/mm2
D = 83mm
σMx = (3*Mx)/(H*L2) = (3*726800)/(10*1402) = 11.2 kg/mm2

## Slide 59
Appendix
Friction Calculation

## Slide 60
M16 Bolts

## Slide 61
M16 Bolts
Preload = 12946 kg
Friction force = 12946*0.4 = 5180 kg

## Slide 62
1 Spring between outer plate to frame
2 Springs – 1 between each plate and frame
X friction force = Fx
Y friction force = Fy
Fx2+Fy2=51832
X friction force = Fx
Y friction force = Fy
Fx2+Fy2=51832

## Slide 63
Bolt Force VS Displacement

## Slide 64
60g Load

## Slide 65
Bolt friction force [kg]
Inner Plate

## Slide 66
Bolt friction force [kg]
Inner Plate

## Slide 67
Bolt axial forces [kg]
Outer Plate

## Slide 68
Bolt axial forces [kg]
Outer Plate

## Slide 69
90g Load

## Slide 70
Bolt friction force [kg]
Inner Plate
Max applied Load - 0.8*90g = 72g

## Slide 71
Bolt friction force [kg]
Inner Plate
Max applied Load - 0.8*90g = 72g

## Slide 72
Bolt axial forces [kg]
Outer Plate
Max applied Load - 0.8*90g = 72g

## Slide 73
Bolt axial forces [kg]
Outer Plate
Max applied Load - 0.8*90g = 72g

## Slide 74
Displacement magnitude [mm]
Plates move together – No slip
Max applied Load - 0.8*90g = 72g

## Slide 75
M18 Bolts

## Slide 76
M18 Bolts
Preload = 15600 kg
Friction force = 15600*0.4 = 6240 kg

## Slide 77
1 Spring between outer plate to frame
2 Springs – 1 between each plate and frame
X friction force = Fx
Y friction force = Fy
Fx2+Fy2=62402
X friction force = Fx
Y friction force = Fy
Fx2+Fy2=62402

## Slide 78
Bolt Force VS Displacement

## Slide 79
60g Load

## Slide 80
Bolt friction force [kg]
Inner Plate

## Slide 81
Bolt friction force [kg]
Inner Plate

## Slide 82
Bolt axial forces [kg]
Outer Plate

## Slide 83
Bolt axial forces [kg]
Outer Plate

## Slide 84
Displacement magnitude [mm]
Plates move together – No slip

## Slide 85
90g Load

## Slide 86
Bolt friction force [kg]
Inner Plate
Max applied Load - 1*90g = 90g

## Slide 87
Bolt friction force [kg]
Inner Plate
Max applied Load - 1*90g = 90g

## Slide 88
Bolt axial forces [kg]
Outer Plate
Max applied Load - 1*90g = 90g

## Slide 89
Bolt axial forces [kg]
Outer Plate
Max applied Load - 1*90g = 90g

## Slide 90
Displacement magnitude [mm]
Plates move together – No slip
Max applied Load - 1*90g = 90g

## Slide 91
Pin angle [deg]
80mm
Tan(0.0278) = X/80
X
X = 0.039mm
There is space of 0.1mm , so there will not be any moment on the Pin.